## Slide 1: Andrew Node-DVB-T Introduction

## Slide 2: DVB-T Background Information
DVB-T networks can be planned in the same way as analogue networks, using an individual set of radio frequencies for each transmission site.
  Migration is inherent in the system design
Delayed signals arriving within the guard interval can be beneficial to a Coded Orthogonal Frequency Division Multiplex (COFDM) receiver, rather than interfering as with analogue signals.
  Simulcast and multi-path are acceptable
Single Frequency Networks (SFN) techniques can be used to fill gaps in coverage on both a small and large scale
  F1-F1 Repeaters can be an important network component

## Slide 3: DVB-T Background Information
Coded Orthogonal Frequency Division Multiplex (COFDM) has many options for flexibility:
  Number of Carriers: 8k-mode (896 µs) and 2k-mode (224 µs).
  Modulation Schemes: QPSK, 16-QAM and 64-QAM
  Bandwidth: 8MHz (preferred), 7MHz and 6MHz optional
  Guard Intervals:
Note: This guard interval is not enough to use most repeaters
All other guard intervals are acceptable

## Slide 4: DVB-T C/N Requirements
Note: C/N dictates what feedback level is acceptable for F1-F1 repeaters
High priority requires a gain margin > C/N >15dB
C/N requirements are higher for high priority signals than low priority signals

## Slide 5: General Repeater Remarks
An off-the-air RF repeater needs sufficient downlink input signal from the serving transmitter
The selected repeater type should be capable of operating close to its rated power (limited by isolation usually)
Antenna selection is important for DVB-T applications. Be aware the value of antenna gain as it is (nearly) intermodulation free. Antennas are much larger at lower frequency than higher frequency for the same gain

## Slide 6: Repeater Setup Definitions
Covered Area
Path Loss
Coverage
Antenna
DVB-T Transmitter
Repeater
Antenna
Isolation
Donor
Antenna

## Slide 7: Isolation
Antenna isolation
  Can’t be calculated exactly, but may be estimated
  Varies with frequency and condition
  Is impacted by the environment it is in
The higher the front-to-back ratio antenna are better
Shielding grids may be used between the antennas

## Slide 8
Interference Cancellation
The Node-DVB-T has integrated ICE (Digital Interference Cancellation Equipment) algorithms are based on adaptive filtering techniques.
This filter adapts to the dynamic multipath structure of the leakage signals and cancels them out.
Node-C’s ICE allows the unit to operate at negative gain margins while preventing oscillation and preserving wave form quality.
Node-DVB Gain Margin Standard Gain Margin
  Gain = Isolation + 20dB Gain = Isolation –15 dB
  Gain Margin (Node-C) = -20dB Gain Margin = +15dB
  Improvement = 35dB

## Slide 9
16 MHz instantaneous bandwidth
35 dB cancellation (65 dB isolation for 85dB of gain)
Automatic setup and continuous optimization
Interference Cancellation

## Slide 10: RF Gain
In DVB-T systems the optimum gain setting is as follows
  In ICE enabled systems the gain limited by
    Isolation + 20 dB or Hardware Power or Hardware Gain
  Example:
    Downlink input level from donor antenna: -50 dBm
    Rated output power per channel: +33 dBm
    Isolation: +70 dB
    Isolation limited gain = 70+20 = 90dB
    Hardware Power limited gain = 33dBm
    Hardware Gain limited gain = 33+50 = 83dB ≤ 85 dB
    Actual Gain setting = 83dB
Limit

## Slide 11: Node DVB-T Basic Specifications
Power: 1-20W average
Gain 50-85dB
Bandwidth/Module: 1 or 2 * 8MHz blocks (3 blocks in roadmap)
Expansion 2 modules possible (up to 6 blocks per unit)
Raster: Variable
Filtering: Selectable digital filter
Setup: Possible measurement receiver
Isolation: Interference cancellation
Supervision Remote via a GSM/UMTS modem
User Interface: Local and remote web based (http)
Supervision: SNMP or SMS for connectivity

## Slide 12: Node-DVB-T Unit
Primary Channel Module
Filter (6-16MHz)
Interference canceller
Controller
Secondary Channel Module
Filter (6-16MHz)
Interference canceller
Linearized
Multi-carrier
Amplifier
Power
Supply
Input and Output RF Filters
IP-65 Outdoor Cabinet
Most components are field replaceable.

## Slide 13
ANDREW CORPORATION
One Company. A World of Solutions.
Notes: <number>
<footer>
<header>
<date/time>